## Slide 1: Multi-model Intercomparison Project on the Saskatchewan-Nelson-Churchill River Basin (Nelson-MiP project)
Monthly meeting - 11 March 2020
Manitoba Infrastructure

## Slide 2: Agenda
Selection of natural gauge stations for calibration/validation for Phase 0 & Phase 1
Decision on time periods for model calibration/validation
Discussion on a standardized meteorological forcing data: WFDEI-GEM-CaPA vs ERA5
Discussion on routing scheme and geophysical input data
Deliverables for next meeting

## Slide 3: Selection of gauge stations for calibration/validation (Phases 0 & 1)
Search criteria:
Station == Natural
Data Period == 1970 to 2016
Total Years >= 35
Drainage area >= 200 km2
+
Stations submitted but not meeting search criteria
291 (natural) gauge stations identified + 11 stations added

## Slide 4: Selection of natural gauge stations for calibration/validation (Phases 0 & 1)
Sub-basins | Number of WSC natural stations
Assiniboine | 32
Lake Winnipeg | 28
Winnipeg river | 13
Upper Churchill | 20
Lower Churchill | 4
Saskatchewan river | 94
Red River | 23
Nelson river | 12

## Slide 5: Selection of natural gauge stations for calibration/validation - continuous vs seasonal
Sub-basins | Number of WSC natural stations
Assiniboine | 32
Lake Winnipeg | 28
Winnipeg river | 13
Upper Churchill | 20
Lower Churchill | 4
Saskatchewan river | 94
Red River | 23
Nelson river | 12

## Slide 6: Selection of natural gauge stations for calibration/validation (Phases 0 & 1)
Sub-basins | Number of USGS stations
Assiniboine | 11
Lake Winnipeg | -
Winnipeg river | 9
Upper Churchill | -
Lower Churchill | -
Saskatchewan river | 1
Red River | 55
Nelson river | -

## Slide 7: Time periods for calibration/validation
Calibration
No calibration for SUMMA

## Slide 8: Time periods for calibration/validation
Validation

## Slide 9: Time periods for calibration/validation
Chart: Annual Rainfall
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Annual | -19.4073 | 2.3684 | 60.2089 | 29.0276 | 15.893 | 24.1818 | 54.7133 | -32.6945 | -4.5814 | -32.9647 | -44.2064 | 36.0581 | -48.8332 | 0.83732 | -46.2501 | -64.1382 | -32.8071 | -17.1208 | -31.3998 | -3.4922 | 67.1834 | -24.6744 | -38.007 | -67.2806 | -11.7385 | 90.9169 | -13.4105 | 28.5243 | 24.2843 | 3.4293 | 75.9729 | -46.3055 | -8.7126 | -49.2282 | 26.8229 | -16.9949 | 28.3159 | -27.8606 | -25.4015
Wet
Calibration | Validation
1981-1985 (wet) | 1986-1990 (Dry)
1991-1995 (Dry) | 1996-2000 (wet and Dry)
2001-2005 (Wet and Dry) | 2006-2010 (Wet)
2011-2018 (Wet and dry) | 
The wet and dry years selection is based on precipitation fields derived from the HydroGFD met. forcing product

## Slide 10: Time periods for calibration/validation
Chart: 
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Spring | -38.1767 | -20.5179 | 21.8195 | -2.1876 | 0.084527 | 10.1172 | 25.9592 | -11.8059 | 4.473 | -8.079 | -6.6958 | 15.8555 | -8.6052 | -25.4392 | -12.591 | -25.7882 | -9.4055 | -25.771 | -20.518 | 20.5261 | 5.3781 | 18.2257 | -7.0794 | -11.7121 | 23.3873 | 6.3292 | 4.8807 | 29.63 | -19.3657 | 4.7237 | 24.172 | -6.5752 | 8.6003 | -10.4342 | 6.896 | -7.9749 | 1.5295 | 4.1783 | -29.6499
Chart: 
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Winter | -8.7396 | 1.5906 | 16.1148 | 14.3623 | 0.15414 | 1.9309 | 2.2109 | 4.2236 | -5.0827 | 7.1449 | -1.7121 | -6.7155 | -2.5653 | -12.7424 | -10.6159 | -1.393 | 4.1286 | -1.5685 | -1.2706 | -8.4278 | -1.2559 | -5.0139 | -11.5181 | -10.7562 | -1.6261 | 18.968 | 9.4601 | 0.75301 | -0.01774 | 6.5223 | -5.2823 | -3.0982 | -8.2042 | -5.4296 | 16.1373 | -2.8577 | -2.3419 | 3.3428 | 4.6681
Wet
Wet
Dry
Dry

## Slide 11: Standardized meteorological forcing data
We have to choose between WFDEI-GEM-CaPA and ERA5
WFDEI-GEM-CaPA (https://doi.org/10.5194/essd-2018-128)  3-hourly, 0.125ᵒ ~ 10 km, 1979-2016 (variables are: huss, pr, ps, rlds, rsds, sfcWind, tas)
ERA5 (https://www.ecmwf.int/en/forecasts/datasets/reanalysis-datasets/era5)  1-hourly, ~31km-grid, 137 levels from surface up to 0.01hPA (~ 80 km), 1979-near real time
 | ERA5 | WFDEI-GEM-CaPA | NCEP-CFRS | Standard MiP data
HYPE | X |  |  | X
SWAT-GIW |  | X | X | 
SWAT-GWF |  |  |  | 
VIC |  |  |  | 
HEC-HMS | X |  |  | X
SUMMA | X |  |  | 
WATFLOOD-MH |  |  |  | 
RAVEN |  |  |  | 
HBV-EC |  |  |  | 
WATFLOOD-MI |  |  |  | 
MESH |  | X |  | 
SWAT-RRB |  | X |  | X
Noah-MP |  |  |  | 

## Slide 12: Hydrologic routing scheme
We should decide on using a standardized routing scheme or not.
All groups were tasked to consider offline routing advantages/ disadvantages
Bryan Tolson’s group (UWaterloo) offers to produce a routing scheme (including lakes) if all modelers will use it.
If Bryan idea is accepted, we should also decide whether the routing scheme shall be derived using HydroSHEDS 3-arc sec DEM (~90m) (https://hydrosheds.cr.usgs.gov/dataavail.php) or MERIT Hydro 3-arc sec data products (https://doi.org/10.1029/2019WR024873).

## Slide 13: Hydrologic routing scheme
The discretization methodology can be applied for any user provided DEM
The resolution of subbasins and lakes represented can be customized
The outputs of the discretization are a vector-based routing network with complete information needed for lakes and river hydrologic routing
RAVEN is used to do the routing simulation

## Slide 14: Routing scheme and other geophysical inputs
Land use/ land cover: North American Land Change Monitoring System (NALCMS)
NALCMS is provided at 250m and 30m spatial resolution, contains 19 land cover classes, and is publicly available from http://www.cec.org/tools-and-resources/map-files/land-cover-2010-landsat-30m.
Soil data: Global Soil Dataset for Earth System Modelling (GSDE)
GSDE is provided at 30 arc-second resolution (~1km), and contains 11 types of soil general information for soil profiles and 34 soil properties for 8 depths up to 2.3 m. It can be downloaded from http://globalchange.bnu.edu.cn/research/soilw#download.
All groups were tasked to explore soil datasets & provide recommendations.

## Slide 15: Deliverables & Follow-up
All modellers should prepare a 5-min presentation of their model for the next meeting. The 1-3 slides presentation should be sent to Hervé by April 1st 2020 at the latest.
Next meeting scheduled for Wednesday April 8 @10:00AM MST